## Slide 1: How CD and DVD Players Work
M. Mansuripur
Optical Sciences Center
The University of Arizona
Tucson, AZ 85721
<masud@u.arizona.edu>
January 22, 2003

## Slide 2: Abstract
Everyone is familiar these days with Compact Disk (CD) and Digital Versatile Disk (DVD) systems. In case familiarity has bred contempt for these marvels of modern technology, we will try to explain in simple terms the complex set of ideas and techniques that have made possible the construction of these Optical Data Storage devices. Information, be it analog (such as voice, still images, video) or digital (e.g., text, computer files, internet traffic) can be represented in binary format as a string of 0's and 1's. These binary strings can be stored on optical disks and retrieved (for reproduction) using lasers and other sophisticated opto-electronic instruments. In this presentation we describe methods of conversion of the various forms of information into binary sequences, discuss methods of storing these sequences on CD and DVD platters, and explain how this information is recovered/reconstructed during playback.

## Slide 3: A Little History
The history of the compact disk (CD) started in the 1970’s with the videodisk in the form of Video Long Play (VLP) read-only systems. The videodisk did not become a commercial success, even after write-once optical disks of different formats and sizes were introduced. These were analog systems. In 1982 the CD-DA (compact disk-digital audio) was introduced to the market jointly by Phillips and Sony. It stored a high-quality stereo audio signal in a digital format. These systems became a huge success. In 1985, the technology was extended to computer storage, again in a collaboration between Phillips and Sony. This was called a CD-ROM (compact disk-read only memory). Early in 1995, two major groups were competing to develop the next generation of high-density compact disks. Under the partnership of Philips and Sony, there began the development of one such format. Concurrently, a group led by Toshiba and Time Warner was working on another format. In September of 1995 the two camps agreed to develop a single standard for a high-density compact disk. The first DVD-video players were sold in Tokyo in November’96, followed by their US introduction in August’97.

## Slide 4: CD Under a Microscope
Track direction
Spiral track
Low-magnification (32) image of a CD showing an edge of the data zone.

## Slide 5: How Small are the Pits on a CD?
Cotton thread (150mm)
Human hair (75mm)
Dust (40mm)
Fingerprint (15mm)
CD pit (0.5  2mm)

## Slide 6: Track Density and Data Density
The CD is 12 cm in diameter, 1.2 mm thick, has a center hole 1.5 cm in diameter, and spins at a constant linear velocity (CLV) or constant angular velocity (CAV).
There is only one track on the optical disk and all data are stored in a spiral of about 2 billion small pits on the surface. There are about 30,000 windings on a CD - all part of the same track. This translates into about 16,000 tracks per inch and an areal density of 1 Mb/mm2.
The total length of the track on a CD is almost 3 miles.

## Slide 7: CD Versus DVD

## Slide 8: CD in Cross-section
A CD can store up to 74 minutes of music, so the total amount of digital data that must be stored on a CD is:
2 channels  44,100 samples/channel/second  2 bytes/sample  74 minutes  60 seconds/minute = 783,216,000 bytes
To fit more than 783 megabytes onto a disk only 12 cm in diameter requires that the individual bits be very small.

## Slide 9: Different Types of DVD

## Slide 10: Inside a CD Player

## Slide 11: Optics of Readout

## Slide 12: Focused Laser Beam Reading the Pits on a CD Surface
The laser beam (wavelength ~ 780 nm) is focused onto the data side of the disk (focused spot diameter ~ 1mm). The laser moves in the radial direction over the fast spinning disk and scans the data track.
Pits are 120 nm deep and 600 nm wide. Laser beam scatters when it scans a pit, which translates into a drop in reflected beam intensity.

## Slide 13: Why Focus the Laser Light through the Substrate?

## Slide 14: Three-beam Tracking
On the top and bottom frames, the central spot B has drifted to one side of the track and the modulation is greatest in one of the side beams A or C. In the center frame, the central spot B is correctly located over the track and the modulation from the central spot is a maximum.

## Slide 15: Focus Actuator
Inside the drive, the disk and the drive's optics are separated by a distance of about 1 mm, making mechanical interaction and crashes, even with wavy disks and imperfect clamping almost impossible.

## Slide 16: Automatic Focusing

## Slide 17: Automatic Focusing

## Slide 18: Automatic Focusing

## Slide 19: How Many 8-letter Words Are There?
AAAAAAAA
AAAAAAAB
AAAAAAAC
.
BROADWAY
.
CONSTANT
.
.
WILDCATS
.
ZZZZZZZZ
00000000
00000001
00000010
.
00100010
.
01001011
.
.
11100010
.
11111111
28 =256
268 =208,827,064,576

## Slide 20: The ASCII Code
A  00101101
B  00101110
.
Z  11011001
0  11011100 1  01010101
2  10101111
.
9  11001100
?  10101001
 00101001
(  11100010
.
.
Any English text can therefore be translated into the language of 0’s and 1’s (the Binary Language) with the aid of the ASCII code.

## Slide 21: Audio Signal

## Slide 22: Electrical Waveform

## Slide 23: Sampling and Analog to Digital Conversion (ADC)
As the sampling rate and precision of analog to digital conversion increase, the fidelity (i.e., the similarity between the original wave and the “digitized” wave) improves. In the case of CD sound, the sampling rate is 44,100 samples per second and the number of gradations is 65,536 (corresponding to 16 bits per sample). At this level, the playback signal so closely matches the original waveform that the sound is essentially perfect to the human ear.

## Slide 24: Translating Binary Digits to Pits

## Slide 25: Mastering and Pressing Disks

## Slide 26: Mastering and Pressing Disks
Mastering involves physical transfer of the data into the pits and lands. First, a layer of light-sensitive photoresist is spin-coated onto the clean glass master-disk from a solvent solution. Then, the photoresist is exposed to a modulated beam of a short-wavelength light, which carries the encoded data. Next, the master is developed in a wet process by exposing it to the developer, which etches away exposed areas thus leaving the same pattern we will find later on the CD. Next, the master is coated (using electroplating technique) with a thick (about 300 mm) metal layer to form a stamper - a negative replica of the disk. The photoresist layer is destroyed during this process, but the much more durable stamper is formed and can be used for CD replication. Usually, a stamper can be used to produce a few tens of thousands CDs before it wears out. Finally, the process of injection molding is used to produce a surface of the compact disk. Hot plastic (PC) is injected into a mold, and then is pressed against the stamper and cooled, resulting in the CD. At the very end, the pits and lands on the surface of a CD are coated with a thin reflective metal layer (aluminum), then coated with lacquer and supplied with the label.

## Slide 27: Speed Rating of CD-ROM Drives
The speed ratings of CD-ROM drives are based on comparison with the first generation drives with the data transfer rates of 150 KB/s or 1X. Today's drives operate at more then 32X boosting data transfer rates beyond 4.8 MB/s, and the improvement has mostly come from the increase in spin rates. The other components have mostly remained unchanged. It seems at this point, that further increase in spindle speed may be impractical due to loss in drive performance.
Previously, CD-ROM drives (slower than 12X) were designed on the basis of the constant linear velocity (CLV) principle, where the angular speed of the drive (rpm) was continuously adjusted following the read head to keep the laser spot moving over the disk surface at constant velocity. This provided uniform spacing of the pits along the track and a constant data transfer rate independent of head positioning over the disk. At some point, this principle was sacrificed to keep up with the need for faster motors, which is much easier to achieve with the constant-angular speed motors. The newest CD drives operate at constant angular velocity (CAV). Now, the transfer rate is a function of the data radius. This also means that the average data transfer rate of the drive is much lower than the drive's maximum rate specified by its X-rating.

## Slide 28: CD vs. DVD
● 74 min. capacity=
(Beethoven’s 9th)!
● 1x by definition
● 1x = 1.23 Mbit/s
● linear V = 1.2 m/s
● >12x = CAV
● 780 nm laser
● 700MB
● 1x-72x speeds
● 4.7 GB
● 1-4x Original
● 4-10x High speed
● 12-24x Ultra speed
● 32x Ultra Speed+
● 4.7 GB
● 18-20x
● 11 Mbit/s
● 650 nm laser
● 25 GB (1-layer)
● 50 GB (2-layers)
● 1x = 36 Mbits/s
● 1x–14x speeds
● 405 nm laser