## Slide 1: Estimation of Fundamental Natural Frequency, Damping Ratio and Equivalent Mass
421L/521L (Lab 8)

## Slide 2: Single DOF Modeling
E, I, L, ρ
E, I, L, ρ
M
k
c
x
mx”+cx’+kx = f(t)
x(t) = Aexp(-ξωnt)COS(ωnsqrt(1-ξ2)t- ψ)+Bsin(ωt)
Time response = Transient response + Forced response(sinusoidal)
Where,
ωn=sqrt(k/m), undamped natural frequency, rad/s
ξ =c/sqrt(2mk), damping ratio
ωd=ωnsqrt(1-ξ2), damped natural frequency, rad/s
k, stiffness, N/m
m, mass, kg
c, damping coefficient, N/(m/s)
E: Young’s modulus
I: Moment of inertia
L: length
ρ: mass per unit length
Cantilever
Fixed-Fixed
accelerometer

## Slide 3: Visualization of responses
Exponential part
Sinusoidal part
Transient
response
Forced response
(Sinusoidal input)
Transient response
+ Forced response

## Slide 4: Experiment
Identify the fundamental mode characteristics using logarithmic decrement
Mount Accelerometer onto beam
  End for cantilever beam
  Center for fixed-fixed beam
Excite beam by applying ‘impulse’ or initial displacement
  Observe transient response (No forced response)
Collect time response
Pick two peaks and measure amplitude and period
Find natural frequency, damping ratio
Find equivalent mass from beam equation
Find damping coefficient and stiffness

## Slide 5: ?
Equivalent mass and natural frequency estimation by Rayleigh method (See the handout)
  Cantilever Beam
  meq = 0.2235ρ L
  ωn=3.6639sqrt(EI/(ρL4)) rad/s
  Fixed-Fixed Beam
  meq = 0.3836ρ L
  ωn=22.373sqrt(EI/(ρL4)) rad/s
Does your measurement match to your estimation?
  Show your measurement and measured value
What if you count the mass of the accelerometer?

## Slide 6: Experimental setup: Cantilever Beam
Aluminum Beam
  Thickness = 4.84mm
  Width = 19.09mm
  Length = 640mm
Accelerometer is mounted at the end of the beam
Mass of accelerometer = 7.83 gram

## Slide 7: Cantilever Beam
NOTE: X1,2 = time in s, y1,2 = acceleration in g, (m = ‘mili’)

## Slide 8: Work Sheet: Cantilever Beam
# | Item | Unit | Value
A | Time @ peak #1 | s | 
B | Time @ peak #2 | s | 
C | Amplitude @ peak #1 | g | 
D | Amplitude @ peak #2 | g | 
E | Time between A and B | s | 
F | Number of periods between A and B |  | 
G | Period of oscillation, E/F | s | 
# | Item | Unit | Value
H | Damped natural frequency, wd | rad/s | 
I | Natural frequency, wn | rad/s | 
J | zeta |  | 
K | Equivalent mass, meq | kg | 
L | Stiffness, k | N/m | 
M | Damping, c | N/(m/s) | 
N | Natural frequency estimation by Rayleigh method | rad/s | 

## Slide 9: Experimental setup: Fixed-Fixed Beam
Aluminum
  Thickness = 4.84 mm
  Width = 19.09 mm
  Length = 640 mm
Accelerometer is mounted at the center
Mass of accelerometer = 7 .83 gram

## Slide 10: Fixed-Fixed Beam
NOTE: X1,2 = time in s, y1,2 = acceleration in g, (m = ‘mili’)

## Slide 11: Work Sheet: Fixed-Fixed Beam
# | Item | Unit | Value
A | Time @ peak #1 | s | 
B | Time @ peak #2 | s | 
C | Amplitude @ peak #1 | g | 
D | Amplitude @ peak #2 | g | 
E | Time between A and B | s | 
F | Number of periods between A and B |  | 
G | Period of oscillation, E/F | s | 
# | Item | Unit | Value
H | Damped natural frequency, wd | rad/s | 
I | Natural frequency, wn | rad/s | 
J | zeta |  | 
K | Equivalent mass, meq | kg | 
L | Stiffness, k | N/m | 
M | Damping, c | N/(m/s) | 
N | Natural frequency estimation by Rayleigh method | rad/s | 

## Slide 12: Different material?
Repeat the experiment with Steel and any nonmetal material
Compare the result