Opti 521:  Paper Review by Mike Dowler

Paper Title:  “Development and Testing of a Synchronous-Scanning Underwater Imaging System Capable of Rapid Two-Dimensional Frame Imaging”

Authors:  T. Kulp, D. Garvis, R. Kennedy, T. Salmon, and K. Cooper

Published in Applied Optics, Vol 32, No. 19 (1 July 93)

Summary

Underwater imaging presents many challenges in the fields of optics, optomechanics, and sensor systems.  Despite all the technological advances in optics and sensors, scatter remains one of the hardest problems to overcome, because of water’s extremely buoyant qualities—things can remain in suspension readily and scatter light.  This results in a very dark underwater environment so that artificial lights are usually mandated for successful imaging; but these also suffer from scattering, reducing the contrast available to the sensor.  A fairly advanced approach that has developed in the last 2 decades involves using a laser to illuminate a small spot in the target area.  This spot is raster scanned across the entire target area of interest and a sensor is slaved to sense the reflected light, similar in principle to a LADAR system but reflected energy is the metric instead of ranging (via timing the pulse returns).  This technique, referred to as an underwater laser-imaging system (UWLIS) has the potential for overcoming much of the scattered light problem, but introduces other challenges in optomechanical engineering.  The authors of this paper have been working on a system at Lawrence Livermore National Laboratory that is described in this paper.  A solid description of the apparatus is presented, however only qualitative results are presented, with several problems in the way the water treatments (which were supposed to closely simulate typical natural turbid water conditions) were handled and explained.

Introduction

The UWLIS device is eventually intended for use by Remotely Operated Vehicles (ROVs) performing deep underwater salvage operations.  The goal is to be able to perform imaging at a distance of 300 m, however the authors point out that even ranges of 60 to 80 m would enable tremendous savings in underwater operations.

Typical existing imaging systems for these applications consist of floodlights to illuminate the target with a variety of camera options.  The effective range of these systems is generally limited to about 2 attenuation lengths (AL) and they don’t really work when the common volume scatter variation (so called because the imaging cone from the camera and the cone of light from the illumination system share the same volume—causing scatter back into the camera system) exceeds the contrast of the target (and hence swamps the sensor).  With a laser system, there is a very small overlap length of the two beams, minimizing common volume scatter.  In theory, these systems can operate up to 7 AL and are practically limited by the amount of power available from the laser and the photon/electrical noise of the detector, as this paper shows.  The wavelength of the laser needs to be in the blue-green regime, as these are the least scattered wavelengths because of the path length—finding compact high power lasers in these wavelengths can be a significant challenge (especially in 1993).  The amount of power available and sensor sensitivity affect the amount of time for the sensor integration; this can affect the rate of scanning of the system and cause problems for video imaging types of speeds.  Additionally, fairly narrow fields of view must be used.

UWLIS Imager

This particular device is the latest iteration of an ongoing concept exploration at Livermore.  In this newest edition, the laser transmission and signal return paths are completely separate.  The raster scanning results in two mirrors scanning at two different rates.  The mirrors consist of beryllium substrates with aluminum reflective coatings of 92% (this was surprising because power seems to be a major issue with this device and much better coatings are readily available).  The horizontal scanning uses a sinusoidal pattern of 3933 Hz while the vertical scan is a sawtooth pattern at 60Hz, giving a FOV of 18° by 14°.  The laser used was an Argon-Ion 5-7 Watt system.  The sensor was an Image Dissector Tube (IDT) which consisted of a photo multiplier tube with a cascade type dynode chain (for maximum sensitivity), whose IFOV is raster scanned.  The target region is imaged onto the face of the IDT with a f/1.2 50 mm camera lens, giving an IFOV of 10.6 mrad, which is 10X that of the laser.  In order to save development costs and schedule, an existing raster scanning system was used from an Inframetrics IR single-detector camera.  The positions of both mirrors was sensed by a pair of optical sensors measuring the deflection of a light beam off the back of the mirrors.

The IDT sensor assembly was mounted outboard of the laser transmitter assembly, at an angle coincident with the target range, and was changed as the range was changed.  Plexiglas windows with silica window inserts were used around the sensor and laser transmitter and were the only parts of the device in contact with the water, mounted at the top of the test tank.  An equation for the power reflected from the target (“return signal”) was shown, which was a summation of the power of each laser line multiplied by the optical transfer efficiency of the transmitter optics, the square of the seawater transmittance, the optical transfer efficiency of the receive optics, the target reflectance and the solid angle of the return optics.  It is important to note that the power is a linear relation to all these factors except the water transmittance.  An expression was also given for the signal to noise ratio, and the two were related such that one could calculate the required power for a given signal to noise.  It was pointed out that one could average frames to improve the signal to noise at the sacrifice of speed.  This leads to limitations of allowed movement for both the optical platform and the target area.  A very high contrast target was used ( however, the authors pointed out how most salvage targets are extremely low contrast) consisting of 112cm square metal plate with an Air Force resolution target on it.

Test Conditions

The in-water test consisted of the apparatus mounted on a crane suspended into the top of a 6m diameter by 15m (holding ~400,000 ltrs) tall free ascent training tank located at 1) the Naval Amphibious Base at Coronado, CA and 2) the Navy Salvage and Diving Training Facility at Panama City, FL.  Maalox was added to the tank to increase water scattering and nigrosin dye was added to increase the water absorption.  Ten different levels of water turbidity/absorption were simulated, ranging from clear (AL .98) to an attenuation length of 7.6 (other values were AL 1.8, 2.5, 2.7, 3.8, 4.6, 5.1, 5.8, 6.3, 6.9).  It was found that the increase in scattering coefficient Δs(536nm)  =  1.0 m-1 for 20 parts per 106 of Maalox.  The scattering coefficient was measured via extinction coefficient with a 10 cm path length transmissiometer; however it operated in the 660nm wavelength band, not in the 500nm band of interest where the laser was operating.  Extrapolations were attempted (work mostly done at Scripps) to related these measurements to the laser bands, but this appeared to be a lot of handwaving and seemed to make their results somewhat questionable (they had another transmissiometer in the correct band but it proved unreliable).  It was discovered that the chlorine in the tank bleached the nigrosin dye, so it was used only for the first three degraded water tests.  Also, the Maalox or the dye had to be added and measured separately since the transmissiometer was incapable of distinguishing the two effects.  It was also discovered that the Maalox particles plated out on the sides of the tank over time, so that it appeared that the water clarity conditions were not completely stable but changing during the tests.

Results

Images were recorded in VHS video, with stills shot from the screen for data.  There was significant image quality losses in the process as can be seen by the images of the test target in the paper.  The study was qualitative only, but suggestions were made about using signal to noise or MTF as possible ways to quantify results.

Eight control imaging devices were set up for comparison purposes.  There were 6 devices relying on the standard floodlight lamps with silicon intensified target (SIT) cameras.  Variations in placement of the light sources, filters, and beam widths were varied.  There were also two set ups using the laser as a light source, one with a beam diverger and one with the scanned laser source.  The set ups using floodlights all performed roughly in the 1 to 2 AL ranges, and were completely limited beyond 2 AL.  Using filters, changing angles, etc didn’t appear to help significantly.  Although separating the light source from the camera seemed to help slightly, it was disappointing to see that the authors didn’t follow through more thoroughly along this line of research.  Using the laser as the illumination source along with the SIT cameras showed medium performance with ranges on the order of 4 AL; the diverging laser source gave a Gaussian profile illumination cross section, while the rastered laser provided a much more spatially uniform illumination.

The rastered laser and rastered sensor IDT technique showed significant range improvements over the standard floodlight-sourced methods, achieving an ultimate range of 6.3 AL.  Up to 4 AL was achieved at real time 30Hz video frame rate, while averaging 8 frames allowed range resolution to 4-5 AL, and averaging 32 frames allowed 5 to 5.7 AL.  The highest range required averaging 128 frames, and motion of either the target or platform could be seen at this slowest rate.  Thus it can be seen that the laser power and signal to noise ratio of the camera were the drivers in terms of achievable range.  Extrapolations were made to try and account for longer distance ranging, however this was never really thoroughly explained and was quite confusing.

Comparison to Other Papers

It was difficult to find much other mention of this topic in the literature; a general web search turned up

http://jaffeweb.ucsd.edu/pubs/UWImage_final.pdf

which gives a very good overall tutorial on the history of underwater imaging, including such advanced topics as range gated imaging and synchronous scan imaging (the topic of the paper being evaluated).  It represents a good alternative explanation of this complex topic, as well as some of the history that led up to the use of lasers as underwater illumination sources.  It is somewhat more tutorial in nature and presents a good accompanying article to the one being evaluated.

Conclusions

I found this paper well written overall and a fascinating optomechanical subject.  It offered a very good introduction and technical description of the device and its particulars, including limitations and shortcomings.  This part is a good tutorial on raster scanned optics.  There is also a good explanation of the sensor system.  However, I was mostly disappointed with the qualitative nature of the results and the poor image quality and data collection that didn’t allow more concrete conclusions, plus the apparent lack of control of the water conditions; this lack of knowledge of the exact turbidity and absorption is an important feature to the entire study because light absorption and scattering in water is so spectrally dependent.  Attempts were made to extrapolate the results but I found these somewhat unsatisfying.  Nevertheless I was impressed that the authors explained these shortcomings honestly and (usually) with clarity.  This entire topic should be revisited today because of the advances in sensor electronics and compact, rugged and more efficient diode pumped lasers.  Also the mirror system should be investigated further to incorporate more solid state devices and get higher reflectivity coatings (thus sparing laser power).

Interested parties for this topic include anyone who has ventured into the watery world and been frustrated by the lack of visibility which obscures everything so effectively.  Salvage experts would also of course be most interested in this topic, because although sonar is an extremely mature and available technology, we as humans are still most curious about how things look.  Sonar, like its cousin radar and ladar are somewhat confusing because they present a range/distance metric instead of a reflectivity metric, as we are used to seeing.  This offers a long range way of seeing underwater for most people who are more concerned with how things actually look.   Another extremely important application is underwater archaeology where a very accurate record of the seabed must be painstakingly mapped and photographed with high resolution, even in turbid waters.

Paper reviewed:

Location of additional paper researched:

http://jaffeweb.ucsd.edu/pubs/UWImage_final.pdf