Requirements Review

Tip / Tilt Mirror System

Mike Borden

OPTI 523

University of Arizona

mborden@optics.arizona.edu

March 11, 2009

Optical:

- Optical Properties will be established from HW 4: Large Mirror Mounting

  - 150 mm nominal beam diameter

  - ∆W < 30 nm rms

    - Includes:  ∆S, mirror flatness, mounting tolerances

  - Ρ = .90 @ 1.06 um

- Operating Wavelength:  400 nm < λ < 1500 nm

Mechanical:

- Tilt Range (Azimuthal):  10° (possibly subject to change)

- Adjustable Angular Resolution:   10 urad

- Alignment stability to 20 urad over 8 hrs

- Alignment stability to 50 urad long term

- Resonant Frequency > 50 Hz

  - Factor of Safety of ~5

- Lightweighted mirror to reduce mass and moment of inertia

- Flexural Interface between mirror mount and mounting structure with actuators

  - Force from actuators and flexure thickness dependent upon one another

Environmental:

- Shock Load:  15G   (based on tip/tilt mirrors in similar applications)

- Operating Temp Range:  -50° C < T 30° C  (aircraft application)

Components Specification:

- Linear Actuators